## Slide 1
Galileo orbit performance monitoring with Where
M. Dähnn, G. A. Hjelle, A.-S. Kirkvik, I. Fausk, M. Ouassou, A. M. Solberg
NKG General Assembly, Helsinki, 6. September 2018

## Slide 2
Part I
Background

## Slide 3
Development
GIOVE A & B
In-Orbit Validation
Initial Services
Exploitation
Phase
Full Operational
Capability
2005/2008
2011-2013
2016
2017
2020
Galileo deployment
Notes: ESA launched two GIOVE satellites in 2005 and 2008 with a representative ground segment and securing the use of the frequencies (not used anymore)
-> testbed for onboard atomic clocks and navigation signal generation / GIOVE satellites are not longer active
in-orbit validation phase: initial validation of the system using four Galileo in-orbit validation IOV satellites (launched October 2011 and 2012)
-> first position fix in March 2013
Initial Services: 15th December 2016 declaration of initial service from European Commission; moving from testing phase to delivering of live service
-> ground infrastructure is operational and ready for positioning, navigation and timing to users; Galileo goes alive
Exploitation phase: routine operations, ground segment maintenance, filling up the satellite constellation
Galileo performance monitoring plays a important role for testing and verifying the initial services and to ensure the provision of high quality satellite data to users.

## Slide 4
Development
GIOVE A & B
In-Orbit Validation
Initial Services
Exploitation
Phase
Full Operational
Capability
2005/2008
2011-2013
2016
2017
2020
Galileo deployment
4 IOV
Notes: ESA launched two GIOVE satellites in 2005 and 2008 with a representative ground segment and securing the use of the frequencies (not used anymore)
-> testbed for onboard atomic clocks and navigation signal generation / GIOVE satellites are not longer active
in-orbit validation phase: initial validation of the system using four Galileo in-orbit validation IOV satellites (launched October 2011 and 2012)
-> first position fix in March 2013
Initial Services: 15th December 2016 declaration of initial service from European Commission; moving from testing phase to delivering of live service
-> ground infrastructure is operational and ready for positioning, navigation and timing to users; Galileo goes alive
Exploitation phase: routine operations, ground segment maintenance, filling up the satellite constellation
Galileo performance monitoring plays a important role for testing and verifying the initial services and to ensure the provision of high quality satellite data to users.

## Slide 5
Development
GIOVE A & B
In-Orbit Validation
Initial Services
Exploitation
Phase
Full Operational
Capability
2005/2008
2011-2013
2016
2017
2020
Galileo deployment
4 IOV
Notes: ESA launched two GIOVE satellites in 2005 and 2008 with a representative ground segment and securing the use of the frequencies (not used anymore)
-> testbed for onboard atomic clocks and navigation signal generation / GIOVE satellites are not longer active
in-orbit validation phase: initial validation of the system using four Galileo in-orbit validation IOV satellites (launched October 2011 and 2012)
-> first position fix in March 2013
Initial Services: 15th December 2016 declaration of initial service from European Commission; moving from testing phase to delivering of live service
-> ground infrastructure is operational and ready for positioning, navigation and timing to users; Galileo goes alive
Exploitation phase: routine operations, ground segment maintenance, filling up the satellite constellation
Galileo performance monitoring plays a important role for testing and verifying the initial services and to ensure the provision of high quality satellite data to users.

## Slide 6
Development
GIOVE A & B
In-Orbit Validation
Initial Services
Exploitation
Phase
Full Operational
Capability
2005/2008
2011-2013
2016
2017
2020
Galileo deployment
24
4 IOV
Notes: ESA launched two GIOVE satellites in 2005 and 2008 with a representative ground segment and securing the use of the frequencies (not used anymore)
-> testbed for onboard atomic clocks and navigation signal generation / GIOVE satellites are not longer active
in-orbit validation phase: initial validation of the system using four Galileo in-orbit validation IOV satellites (launched October 2011 and 2012)
-> first position fix in March 2013
Initial Services: 15th December 2016 declaration of initial service from European Commission; moving from testing phase to delivering of live service
-> ground infrastructure is operational and ready for positioning, navigation and timing to users; Galileo goes alive
Exploitation phase: routine operations, ground segment maintenance, filling up the satellite constellation
Galileo performance monitoring plays a important role for testing and verifying the initial services and to ensure the provision of high quality satellite data to users.

## Slide 7
Motivation – Galileo performance monitoring
testing and verifying the initial services
detecting anomalies (satellite faults)
ensure the provision of high quality satellite data to users
signal-in-space range error is a key performance indicator used from all GNSS
Control segment
Space segment
User segment

## Slide 8
Part II
What is signal-in-space range error (SISRE)?

## Slide 9
What is signal-in-space range error (SISRE)?
Notes: SISRE: modelling errors of the individual ranging measurements related to control and space segment
1. Receiver receives satellite signal and determines the range between the satellite and the receiver. This range is also called pseudorange because the satellite and receiver clock are not synchronized.
SISRE: Statistical uncertainty of the modeled pseudorange related to broadcast orbit and clock information.
Broadcast orbit and clock information depends on control and space segment. SISRE represents the error budget related to control and space segment.
Control Segment: Orbit and clock determination performance, distribution of monitoring stations, and upload capacity
5. Space Segment: Clock stability, satellite antenna variation, signal imperfection and predicability of orbital motion

## Slide 10
What is signal-in-space range error (SISRE)?
SISRE: Statistical uncertainty of the modeled pseudorange related to
errors in the broadcast orbit and clock information.
SISRE
Notes: SISRE: modelling errors of the individual ranging measurements related to control and space segment
1. Receiver receives satellite signal and determines the range between the satellite and the receiver. This range is also called pseudorange because the satellite and receiver clock are not synchronized.
SISRE: Statistical uncertainty of the modeled pseudorange related to broadcast orbit and clock information.
Broadcast orbit and clock information depends on control and space segment. SISRE represents the error budget related to control and space segment.
Control Segment: Orbit and clock determination performance, distribution of monitoring stations, and upload capacity
5. Space Segment: Clock stability, satellite antenna variation, signal imperfection and predicability of orbital motion

## Slide 11
Control segment
Space segment
SISRE
What is signal-in-space range error (SISRE)?
SISRE: Statistical uncertainty of the modeled pseudorange related to
errors in the broadcast orbit and clock information.
Notes: SISRE: modelling errors of the individual ranging measurements related to control and space segment
1. Receiver receives satellite signal and determines the range between the satellite and the receiver. This range is also called pseudorange because the satellite and receiver clock are not synchronized.
SISRE: Statistical uncertainty of the modeled pseudorange related to broadcast orbit and clock information.
Broadcast orbit and clock information depends on control and space segment. SISRE represents the error budget related to control and space segment.
Control Segment: Orbit and clock determination performance, distribution of monitoring stations, and upload capacity
5. Space Segment: Clock stability, satellite antenna variation, signal imperfection and predicability of orbital motion

## Slide 12
Precise (true) orbit
Broadcast orbit

## Slide 13
Precise (true) orbit
Broadcast orbit
along-track
radial
cross-track
.
.
Notes: Radial – vector to the Earth center
Along-track – lying orbital plane and shows more or less in the direction of satellite motion
Cross-track – fulfills a right hand system

## Slide 14
Precise (true) orbit
Broadcast orbit
along-track
radial
cross-track
.
.
Notes: Radial – vector to the Earth center
Along-track – lying orbital plane and shows more or less in the direction of satellite motion
Cross-track – fulfills a right hand system

## Slide 15
Precise (true) orbit
Broadcast orbit
a
r
c
.
.
Notes: Radial – vector to the Earth center
Along-track – lying orbital plane and shows more or less in the direction of satellite motion
Cross-track – fulfills a right hand system

## Slide 16
SISRE computation

## Slide 17
SISRE computation

## Slide 18
SISRE computation
weight factors
Notes: Global averaged SISRE: spatially independent (compared to instantaneous SISRE) – range error across the portion of the Earth in view of the satellite
Weight factors for radial and along-/cross-track errors
- Weight factors depend on:
- GNSS (lower altitude/orbital radius of satellites means lower weight factor)
- Elevation mask

## Slide 19
Part III
SISRE implementation in Where

## Slide 20
SISRE implementation in Where

## Slide 21
SISRE implementation in Where
Notes: Edit: healthy satellites, remove duplicated broadcast ephemeris, choose navigation message (INVA, FNAV), use of observation for validity length
- Orbit: determine broadcast and precise orbit

## Slide 22
SISRE implementation in Where
Broadcast ephemeris:
- IGS MGEX (BRDM) product derived from a subset of IGS stations
Precise ephemeris:
  - IGS MGEX (CODE)
Notes: Edit: healthy satellites, choose navigation message, use of observation for validity length
- Orbit: determine broadcast and precise orbit

## Slide 23
SISRE implementation in Where
Ignore unhealthy satellites
Remove duplicated navigation messages
Select navigation message (INAV or FNAV) and valid navigation record
Remove epochs exceeding validity length of broadcast ephemeris (> 4 hours)
Notes: Edit: healthy satellites, choose navigation message, use of observation for validity length
- Orbit: determine broadcast and precise orbit

## Slide 24
SISRE implementation in Where
Determine broadcast orbit and satellite clock corrections based on GALILEO-OS-SIS-ICD (2015)
Interpolate precise orbit and clocks by using Lagrange and respectively linear interpolation
Notes: Edit: healthy satellites, choose navigation message, use of observation for validity length
- Orbit: determine broadcast and precise orbit

## Slide 25
SISRE implementation in Where
SISRE analysis in Where based on paper of Montenbruck et. al
(2018)
Relate satellite orbit and clock to center of mass by applying antenna phase center offsets
Apply constellation mean clock errors in each epoch
Correct satellite clock correction for differential code biases
Outlier rejection
Notes: Epochwise mean orbit and clock correction: account for different GNSS time scale realization
Precise and broadcast clock correction can be based on different signal-linear combination/Correct satellite clock for DCBs: depend on the precise clock generation (Galileo: E1E5a) -> E1 + BGD and E1E5b + DCB
Data logging errors in broadcast and precise products affect resulting statistics unless the data are rejected (3-sigma range)

## Slide 26
Part IV
Results

## Slide 27
Galileo E1/E5a (FNAV)
Time [GPS]
Δclock [m]
Δradial [m]
Δcross-
track [m]
Δalong-
track [m]
Notes: - In the Galileo open service provides to navigation messages:
FNAV: free navigation message (E5a)
INAV: integrity navigation message (E1 and E5b)
- Half a year with data

## Slide 28
Galileo E1/E5a (FNAV)
Time [GPS]
SISRE [m]
RMS = 0.16 m

## Slide 29
SISRE 95th percentile [m]
E1 E1E5b E1E5a
INAV INAV FNAV
95% SISRE over all healthy satellites and a period of 30 days ≤ 2 m
Galileo-OS-SDD (2016)
Notes: Galileo Open Service definition document defines minimum performance level, where

## Slide 30
SISRE 95th percentile [m]
E1 E1/E5b E1/E5a
INAV INAV FNAV
95% SISRE over all healthy satellites and a period of 30 days ≤ 2 m
Galileo-OS-SDD (2016)
Notes: Galileo Open Service definition document defines minimum performance level, where

## Slide 31
Galileo E1/E5a (FNAV)
Navigation messages
were not refreshed.
Time (May 2017)
Notes: Anomaly: condition during a healthy and trackable satellite exceeds defined thresholds
Galileo navigation message are only valid for 4 hours

## Slide 32
Part V
Conclusion and outlook

## Slide 33
Conclusion and outlook
Where SISRE solution shows comparable results to other studies (e.g. Montenbruck et. al (2018) or Galileo-IS-OS (2018)) with SISRE RMS of 16 cm and monthly 95th percentile of 30-50 cm
Further validation of Where SISRE analysis needed
Improvement of SISRE analysis by quality checking of input data and outlier rejection
Notes: Experience needed for detecting anomalies

## Slide 34
Literature
Galileo-IS-OS (2018): European GNSS (Galileo) inital services – Open service quarterly performance report. January-March 2018.
Galileo-OS-SDD (2016): European GNSS (Galileo) inital services – Open service definition document. Issue 1.0, December 2016.
Galileo-OS-SIS-ICD (2015): European GNSS (Galileo) Open service – Signal in space inferface control document. Issue 1.2, November 2015.
Montenbruck, O., Steigenberger, P., and Hauschild, A. (2018): Multi-GNSS signal-in-space range error assessment – methodology and results. Advances in Space Research, 61(12):3020-3038. DOI 10.1016/j.asr.2018.03.041.
Notes: Heng, L. (2012): Safe satellite navigation with multiple constellations: global monitoring of GPS and GLONASS signal-in-space anomalies. Department of Electrical Engineering, Stanford University.
Montenbruck, O., Steigenberger, P., and Hauschild, A. (2014): Broadcast versus precise ephemeris: a multi-GNSS perspective. GPS Solutions, (19):321-333. DOI 10.1007/s10291-014-0390-8.

## Slide 35
Thank you for your attention!

## Slide 36
22
36
19
26
12
07
08
03
05
09
04
25
24
31
01
30
27
02
A plane
B plane
C plane
Relative RAAN
Relative Mean Anomaly
180°
225°
0°
45°
90°
135°
315°
270°
0°
120°
240°
20
21
15
13
33
Usable satellite (17)
Under commissioning (5)/
Testing (2)
Not usable (2)
11
Galileo satellite constellation
Notes: E14/E18: on elliptic orbits in test mode
E20: has no ephemeris
E22: removed from active constellation for constellation management purposes
E13, E15, E21, E33, E36: under commissioning
RAAN and mean anomaly describes position of satellite
RAAN: right ascencion of ascending node (indicates where the orbital plane crosses the equator)
Mean anomaly: describes the motion of a fictitious satellite, which moves uniformly on a auxiliary circle with the radius a around the geocenter.

## Slide 37
Satellite antenna relation
Broadcast orbit
Precise orbit
Relate orbit and clock differences to center of mass by applying PCOs given by GSC and IGS (igs14.atx)

## Slide 38
Difference between broadcast and precise orbit and clocks
Transformation of orbital differences to local orbital reference frame
Apply constellation mean orbit and clock errors in each epoch
Phase center offset
Broad-cast orbits
Precise orbits
Correct satellit clock for DCBs
Relate orbit and clock differences to center of mass by applying PCOs
, , ,
DCBs
Compute SISRE
, ,
IGS
DLR
IGS
CODE
IGS, GSC
IGS
CAS
Outlier rejection
Montenbruck et. al (2018)
Notes: CODE: Center of Orbit Determination in Europe
CAS: Chines Academy of Sciences
JPL: NASA Jet Propulsion Laboratory
Epochwise mean orbit and clock correction: account for different GNSS time scale realization
Correct satellite clock for DCBs: depend on the precise clock generation (Galileo: E1E5a) -> E1 + BGD and E1E5a + DCB
Data logging errors in broadcast and precise products affect resulting statistics unless the data are rejected (3-sigma range)